## Slide 1: Barbarosa Road / Saur Lane Widening
2022 Bond Program
NB 22-167

## Slide 2: Project Location

## Slide 3: Barbarosa Rd/Saur Ln
Existing Conditions:
2-lane undivided major urban collector
Limited, discontinuous pedestrian facilities
2 signalized intersections
Annual Average Daily Traffic: 11,400 veh/day (2030)
Major thoroughfare between IH 35 and FM 758
Facility serves:
  Single and Multi-family Residential
  New Braunfels National Airport
  Commercial/Retail
  Hospital & Retail Shopping center (2027)

## Slide 4: Barbarosa Rd/Saur Ln
Proposed Conditions:
4-lane major urban collector
Continuous bike and pedestrian facilities
Annual Average Daily Traffic: 18,200 veh/day (2050)
Key Features
  4 lane facility with 12’ lanes
  9 new left turn lanes, 4 new right turn lanes
  New storm sewer
  14’ wide medians or shared left turn lanes
  10’ wide SUP and 6’ sidewalks with green space

## Slide 5: Construction Phasing

## Slide 6: Construction: Phase 1
Existing Conditions
  Common Lanes: 12’ wide
  Shoulder Varies: 0’ - 4’ wide
  Maintaining current day traffic patterns
Construction Phase 1:
  Construct temporary pavement
  No shoulder on eastbound traffic
  No traffic shift
  Common lane widths remain 12’

## Slide 7: Construction: Phase 2
Construction Phase 2:
  Shift traffic
  Erect low profile concrete barrier
  Lanes reduced to 11’ wide in each direction
  Construction begins on westbound lanes, curb and gutter, and sidewalks

## Slide 8: Construction: Phase 3
Construction Phase 3:
  Shift traffic on to newly constructed pavement
  Erect low profile concrete barrier
  Lanes remain 11’ wide in each direction
  Construction begins on eastbound lanes, curb and gutter, and sidewalks

## Slide 9: Environmental Impacts

## Slide 10: NATIONAL ENVIRONMENTAL POLICY ACT (NEPA)
  National Environmental Policy Act (NEPA) Assignment to the Texas Department of Transportation
  The environmental review, consultation, and other actions required by applicable Federal environmental laws for this project are being, or have been, carried out by TxDOT pursuant to 23 U.S.C. 327 and a Memorandum of Understanding dated December 9, 2019, and executed by FHWA and TxDOT.

## Slide 11: Environmental Considerations
Natural Resources
  Land Use
  Air Quality
  Noise
  Water Quality
  Wetlands
  Vegetation and Wildlife
  Geology, Farmlands, and Soils
  Threatened and Endangered Species
Cultural Resources
  Archaeological Resources
  Historical Non-archaeological
  Section 4(f)/6(f) Properties
Social Resources
  Pedestrian and Bicycle
  Economic

## Slide 12: Project Timeline
*Dates subject to change